## Slide 1: Cell preparation for 10X
Diana Burkart-Waco, PhD
dburkart@ucdavis.edu

## Slide 2: Overview
Technology overview.
Single cell isolation.
Sample QC.
  Do I have single cells?
  Are they alive?
  Are they too big?
  Did I isolate the correct cells?
How do I count them?
Methanol Fixation.

## Slide 3: 10X technology

## Slide 4: Sample preparation
10xgenomics.com/
Single cell isolation is key.
No one protocol fits all.
Invest time sample preparation.

## Slide 5: Cell isolation
Cell isolation guides available at:
https://www.support.10xgenomics.com/single-cell-gene-expression/sample-prep/
  Dissociation and preparation depends on cell type.

## Slide 6: Factors influencing success
Cell debris.
Aggregates.
Proper concentration estimates.
Buffer.
Storage.

## Slide 7: Workflow
Single cell suspension
Visually inspect cells
Free of debris
YES
Count
NO
Filter

## Slide 8: Debris
Organic matter left over from dead cells.
Impacts targeted cell recovery.
  Free RNA  noise.
  Hard to obtain cell counts.
  Clog microfluidics
http://www.nexcelom.com/Cellometer-Vision-CBA/

## Slide 9: Cell debris example I
Mouse
Clean DRG sample Noisy sample
Clean DRG sample Noisy sample
Recommended treatment: filtration, centrifuge, add blocking agent.

## Slide 10: Cell debris example II
Human
Clean human sample All debris
Bone shard
Recommended treatment: redo isolation.

## Slide 11: Summary - debris
Work on gentle dissociation cells.
  Ex) Trituration with P-1000 first then P-200.
Filtration (ex, 40 micron strainer).
Density gradient centrifugation.
  Ex) ficoll or sucrose gradient.
Detergents.
Redo cell isolation.
Debris
Debris

## Slide 12: Doublets
Non-single cell clumps.
Integrated into droplets and cannot* distinguish from single cells.
Bad for any single cell experiment.
*Call some doublets in tagged cells (multi-seq or ‘Feature Barcodes’)
Doublet

## Slide 13: Doublets example I
Doublet
Clump
Good sample Many multiplets

## Slide 14: Summary - doublets
Did you fully dissociate your tissue?
Cells can sit too long  clumps.
  Depends on cell type.
  Know the temperature your cells are happy at.
    Ex) some bovine cells like to be warm; neurons RT, etc.
Add blocking agent.
  BSA or FBS (make sure conc. compatible with 10X)

## Slide 15: Dead cells
Single cell suspension
Live / dead staining
Are my cells live?
YES
Count
NO
Redo isolation or dead cell removal

## Slide 16: Assessing cell death
Use cell-impermeant dye or fluorescent labels.
  Automated cell counter okay, but sometimes better by hand.
    Very small cells may stain ‘dead’ automated cell counter.
Cells die during isolation, but also during (improper) cryopreservation.
  Count before and after cryopreservation.
Dead
Dead

## Slide 17: Do I need a clean suspension?
% Reads in cells
Recovery (cells)
Reads in cells.
Targeted recovery.
Digitonin (mimics dead cells) treated cell suspension.
DCR – Dead Cell Removal
CG000130_10x_Technical Note_DeadCell Removal_RevA.docx

## Slide 18: Cell Size and did I isolate the correct cells?
Microfluidics have cell size limit
  40 microns or less.
  Clogs, etc.
Nuclei isolation great alternative to large cells.
Know your cell size.
  Do you have RBC contamination (‘empty’ cells).
Histogram cell size
Small dark cells

## Slide 19: Cell size – example I
Expect cells to be from 2 micron to 20 micron.
Average size 3um.
Two different isolations from same tissue.
Left – small and uniform.
Right – variable sizes.
Tiny cell

## Slide 20: Overview
Technology overview.
Single cell isolation.
Sample QC.
  Do I have single cells?
  Are they alive?
  Are they too big?
  Did I isolate the correct cells?
How do I count them?
Methanol Fixation.

## Slide 21: Cell counting – automated
Countess II (done by DNA Tech).
Pros (+):
  Fast.
  Live/dead cell counts.
  Cell size estimates.
Cons (-):
  Cell size limits (4-60um).
  Performance poor for odd shapes.
  Cell type limitations (DRG…)

## Slide 22: Cell counting – manual
Hemocytometer (customer-supplied counts).
Pros (+):
  Reliable cell counts.
Cons (-):
  Slow?
http://www.wetnewf.org/pdfs/hemocytometer.html

## Slide 23: Cell counting – automated
Pros (+):
  Sort based on characteristics (fluorescence, etc).
  Characterize cells.
Cons (-):
  Cannot provide absolute counts.
  Tends to overestimate cells.
  Concentrate after.
https://www.idexx.com
Flow

## Slide 24: Methanol fixation
Methanol permeabilises cells and dehydrates proteins.
Kills infectious agents, while maintaining cell structure.
Cells stain 100% dead and can be stored for weeks

## Slide 25: Important metrics – 10X
Concentration: 100-2,000 cells per µl.
  700-1,200 cells per µl.
  Count in replicates!
  We require cell counts prior to delivery.
Viability: 70% minimum.
  Nuclei and methanol fixed cells.
Sample buffer.
Cell size and shape..
Treat cells gently.
  Wide bore pipette tips, keep cells on ice, etc.
Credit-10X Genomics

## Slide 26: Chip loading
Very flexible  cell concentration and recovery.

## Slide 27: Cost – 2019 10X Single Cell
Per prep day | Cost
Labor, cell QC, chip | $235
Labor, reagents, instrument use | $1,837
Library prep | Total Cost
1 sample | $2,072
2 samples | $3,909
3 samples | $5,746
UC RATES

## Slide 28: Important resources
10X Genomics
  https://support.10xgenomics.com/single-cell-gene-expression
UC Davis Flow Cytometry
  http://www.ucdmc.ucdavis.edu/pathology/research/research_labs/flow_cytometry/index.html
  Bridget McLaughlin (Technical Director)
UC Davis DNA Technology Core
  http://dnatech.genomecenter.ucdavis.edu/single-cell-analyses/

## Slide 29: Acknowledgements
UC Davis DNA Technology Core.
UC Davis Bioinformatics Core.
10X Genomics.
  Nicole Rapicavoli (Lead Field Applications Scientist).